## Slide 1: AR Wayfinding for Queenstown's Elderly
CDE2501 Sustainable Systems for Liveable Cities
Group 2 — Queenstown
AY 2025-2026 Semester 2

## Slide 2: Site Analysis: Queenstown
Singapore's first satellite town — developed in the 1950s
Mature estate with over 70 years of history
Super-aged: 22.6% of residents are 65+ years old
Part of HDB's Health District @ Queenstown initiative
NUS-NUHS collaboration area for healthy ageing research
URA Master Plan 2019: increased redevelopment, stronger MRT planning, healthcare emphasis

## Slide 3: Site Analysis: Physical Environment
Site area: 159,301 m² | Perimeter: 1,645 m
Elevation range: Min 6.6m, Median 15.3m, Max 24.76m (8.7m difference)
Hilly terrain with constant uphill routes between blocks
Older flat layouts with narrow corridors (insufficient for wheelchairs)
Limited or poorly sheltered walkways between blocks
Cluttered common areas — overflowing recycling, motorcycles on walkways
Dementia Wayfinding Murals at Stirling View (existing community effort)

## Slide 4: Site Analysis: Who Lives Here
22.6% aged 65+ — classified as super-aged estate
65.6% working adults (15-64 years)
Key landmarks: Queenstown MRT, Mei Ling Market & Food Centre, Queenstown Polyclinic
Lions Befrienders and Care Corner — active social service presence
Mixed land use: residential, commercial, health & medical, religious, recreational
Strong MRT connectivity but poor last-mile within the estate

## Slide 5: Problem Statement
"In Queenstown's interconnected HDB blocks, inconsistent level connections
and poor spatial legibility produce unsafe and disorienting navigation
conditions that disproportionately impact wheelchair users, dementia patients,
cane users, and medically challenged elderly residents, heightening fall risk
and undermining barrier-free mobility."
Root causes: 8.7m elevation change, limited ramps, poor signage, narrow corridors

## Slide 6: Problem Analysis: Who Is Affected
Wheelchair users: 8.7m elevation climb, no nearby ramps, constant uphill → limited independence
Dementia patients: repetitive layout, long detour routes → increased confusion, anxiety
Cane/walking aid users: steep terrain, stair-heavy routes → higher fall risk, fatigue
Medically challenged elderly: exhausting travel routes → avoid leaving home, social isolation
Caregivers: physical strain assisting uphill, emotional stress burden
Town Council: resident complaints, upgrade cost pressure, safety liability

## Slide 7: Systems Thinking: Causal Loop Diagram
Reinforcing Loop (R1): Mobility Barriers → Risk of Safety Hazards → Reduced Use of Public Spaces
→ Less Local Stewardship → More Clutter → More Passive Common Areas → More Barriers
Balancing Loop (B1): Mobility Barriers → Demand for Wayfinding Improvements
→ Better Signage → Reduced Safety Hazards → Improved Quality of Life
Our intervention targets B1: improving wayfinding effectiveness to reduce safety hazards

## Slide 8: Framing: Why Digital Wayfinding
Physical infrastructure (ramps, lifts) costs $200-400K per installation, takes years
Signage helps but is static — doesn't adapt to individual needs or conditions
22.6% elderly population needs guidance NOW, not in 5 years
Digital wayfinding: zero infrastructure cost, instant deployment, personalized routes
Collects walking data that INFORMS future physical infrastructure investment
Aligns with Health District @ Queenstown vision of technology-enabled healthy ageing

## Slide 9: Solution: AR Wayfinding App
Flight-tracker AR view: point phone at destination → see name, distance, ETA on camera
Safety-weighted routing: avoids stairs for wheelchairs, steep slopes for elderly
Minimap with heading arrow: always know which direction you're facing
Two profiles: Elderly (1.0 m/s) and Wheelchair (0.8 m/s) with rain mode
Works on any Android phone with GPS + compass — no special hardware needed
Data syncs from Google Drive — updates without reinstalling the app

## Slide 10: Solution: Crowd-Sourced Walking Data
Record labeled paths: testers walk from A to B, GPS breadcrumbs saved every 1 second
Auto-screenshots on heading changes (>30°) + every 10 seconds + manual Snap
Telemetry CSV: GPS, heading, altitude, floor estimate, GPS accuracy, loss detection
Saved paths show where elderly ACTUALLY walk vs. where planners think they walk
Data feeds back to HDB: evidence for ramp placement, walkway sheltering, signage
Share button sends telemetry via Drive/email — no technical knowledge needed

## Slide 11: How It Works: User Journey
1. Open app → data downloads from Google Drive (3MB, takes seconds)
2. Select destination: 'Mei Ling Hawker Centre'
3. App calculates safest route avoiding stairs and steep slopes
4. AR view shows direction arrow on camera — follow it
5. Minimap shows progress with heading indicator
6. Tap 'Record Path' to save the walk for future graph improvement
7. Arrive. Total guided time shown. Path saved for analysis.

## Slide 12: Solution Evaluation: Stakeholder Impact
Wheelchair users: routes avoid stairs entirely → independent mobility restored
Dementia patients: AR arrows + familiar landmarks → reduced confusion
Cane users: flat/gentle routes prioritized → lower fall risk
Caregivers: can send elderly independently → reduced physical & emotional burden
HDB/Town Council: real walking data → evidence-based infrastructure planning
Health District @ Queenstown: technology-enabled ageing in place

## Slide 13: Solution Evaluation: Trade-offs & Limitations
Requires smartphone: many elderly (70-90 years) lack digital literacy
→ Mitigation: family/caregiver sets up the app once, elderly follows AR arrows
GPS unreliable between tall blocks: 10-30m drift in signal shadow zones
→ Mitigation: dead reckoning fallback planned (compass + step counting)
Can't fix physical terrain: if no ramp exists, no alternative path
→ Mitigation: walking data identifies exactly WHERE ramps are needed most
No indoor navigation yet: corridors and lift lobbies need BLE/WiFi positioning

## Slide 14: Impact: Social, Environmental, Economic
Social: reduces isolation (elderly leave home more), builds independence, dementia-friendly
Environmental: encourages walking over motorized transport, zero emissions from app
Economic: $0 infrastructure cost vs. $200-400K per ramp installation
App deployment: free (Google Drive hosting, no server needed)
Data collection: replaces expensive walking audits ($50-100K consultant studies)
Scalable: same app works in any HDB estate — just update the graph data

## Slide 15: Conclusion
Queenstown's elderly face unsafe, exhausting, disorienting daily navigation
Physical fixes (ramps, lifts) are expensive and slow — 5+ year timeline
AR wayfinding provides immediate, personalized, data-collecting guidance
Every walk recorded improves the system — crowd-sourced path optimization
The app doesn't replace infrastructure — it makes infrastructure investment smarter
Digital wayfinding companion for the Health District @ Queenstown initiative